Controlling the motors

- Motors are controlled through the ESCs.
- They work on pulse widths between 1000ys (off) and 2000ys (on) like the RC radio receiver.
- The pulse should be at 50Hz normally (ESC uses an averaging filter if necessary), but it works better if we minimize the effect of the filter. The APM HAL library sends the pulse at 490Hz. The 5-10 pulse that are averaged occur very quickly, this negates the filters effect. (that is good)